DEBUGGING ADS-B RECEIVER EXTERNALLY

POWER
ADS-B
MDA N/W

1. Three LEDs have now been additionally given on the box for aiding the purpose of debugging the ADS-B receiver.
2. The LEDs are colour coded viz. Red, Green and Blue. The LED's indicate status as follows:-
  1. Red LED	-	Power Status.
  2. Green LED	-	ADS-B Message Reception Status.
  3. Blue LED	-	Connectivity with MDA Network.
  Booting Up

1. While booting up, all three LEDs stay on till the time respective control program does not kick in. If the LEDs are ON continuously for a sustained time, they indicate a fault with the system, most probably a software fault.
  Normal Operations
2. Red LED. This LED does not blink and stays permanently on. A glowing LED indicates that the system is powered up and power supply is available. If the LED is OFF, check power supply to the hardware.

1. Green LED. This LED blinks intermittently. It blinks twice for every message received by the system. Blinking of the LED indicates that the system is receiving ADS-B messages and the hardware is working satisfactorily. If no messages are being received by the system, the LED will blink one every minute, to indicate that the hardware is working satisfactorily.
2. Blue LED. This LED blinks periodically. It has various blinking modes. Each mode is made up of two parts. The initial part indicates network connectivity with the MDA network server and the subsequent mode indicates connectivity with MDA database on the remote server. The modes are described below:-
  1. 2 Long and 5 Short blinks	-	Network Connected and connectivity with MDA database established.
  2. 2 Long blinks	-	Network Connected however connectivity with MDA database not established.
  3. 2 Very Long Blinks (2 Sec each)	-	Network down. Not able to ping remote machine.